## Slide 1
M.Tech Program
Advanced Industry Integrated Programs
Jointly offered by University and LTIMindTree
Review III
Deterministic MCP-Driven AI Agents for Ball Bearing Vibration Diagnostics
Arjun V P
T9987
VIT Chennai
Knowledge partner | Implementation partner

## Slide 2
Introduction
Deterministic MCP-Driven AI Agents for Ball Bearing Vibration Diagnostics
INDUSTRIAL CONTEXT
Rolling-element bearings are critical to rotating machinery reliability.
DIAGNOSTIC CHALLENGE
Faults create downtime, cost and equipment-risk; raw vibration is difficult to interpret continuously.
PROPOSED SYSTEM
A deterministic MCP-driven agent combines engineering diagnostics with explainable AI assistance.
DATA FOUNDATION
NASA IMS Run-to-Failure Bearing Dataset → vibration observations → feature-based health assessment
Goal: reliable, reproducible and engineer-facing bearing fault diagnosis

## Slide 3
Objective
Deterministic MCP-Driven AI Agents for Ball Bearing Vibration Diagnostics
Core objective
DETERMINISTIC MCP-DRIVEN AI AGENT
Ball bearing health monitoring + fault diagnosis with consistent and explainable decisions
SIGNAL ANALYSIS
Extract vibration indicators and identify bearing health conditions.
ISO-BASED LOGIC
Incorporate diagnostic principles and deterministic decision criteria.
EXPLAINABILITY
Produce reproducible fault identification instead of relying only on probabilities.
MAINTENANCE SUPPORT
Turn diagnostics into actionable information for reliability teams.
Expected impact: fewer unplanned failures • better maintenance decisions • lower unnecessary maintenance

## Slide 4
Modules to cover
Deterministic MCP-Driven AI Agents for Ball Bearing Vibration Diagnostics
Six-stage project workflow
1. DATA
NASA IMS vibration
2. FEATURES
RMS • Kurtosis • P2P • Crest
3. HEALTH
Baseline deviation + score
4. DIAGNOSIS
Rules / thresholds / ISO
5. MCP AGENT
Tools + structured context
6. VALIDATION
Faults + explanations
END-TO-END OUTPUT
Bearing condition → deterministic diagnostic evidence → explainable maintenance insight
Designed to keep the diagnostic core reproducible while using the agent as the interpretation layer.

## Slide 5
Problem Statement
Deterministic MCP-Driven AI Agents for Ball Bearing Vibration Diagnostics
Why existing approaches are insufficient
UNPLANNED FAILURE
Bearing degradation can become downtime, maintenance cost and reliability risk.
FIXED / MANUAL MAINTENANCE
Scheduled inspection can miss progressive degradation between checks.
RAW TELEMETRY
Vibration signals contain useful indicators but are hard to interpret continuously.
IDENTIFIED GAP
Predictive models may provide a prediction, but an interactive layer is needed to connect diagnostics, trends and maintenance actions.
Need: evidence-based maintenance decision support from historical vibration telemetry.

## Slide 6
Python Modules
Deterministic MCP-Driven AI Agents for Ball Bearing Vibration Diagnostics
Data-to-agent software pipeline
RAW DATA
Vibration files
FEATURES
RMS • Kurtosis • P2P
OBSERVATIONS
Bearing-level records
HEALTH / RUL
Health + prognostics
FASTAPI
Telemetry / requests
MCP SERVER
Diagnostic tools
AGENT
Llama 3.2
FINAL OUTPUT
Maintenance decision support based on deterministic engineering signals and MCP tool results.
Modules remain separable: data → features → health → API → MCP → agent.

## Slide 7
Python Modules
Deterministic MCP-Driven AI Agents for Ball Bearing Vibration Diagnostics
DATA & FEATURE PROCESSING
HEALTH & PROGNOSTICS
data.py → features.py → build_features.py
Ingest and validate files • parse timestamps • extract RMS, Kurtosis, Peak-to-Peak and Crest Factor • build structured features
observations.py → health.py → rul.py / rul_model.py
Convert features into bearing observations • calculate baseline deviation, degradation index and health score • generate/evaluate RUL baseline
APPLICATION & AGENTIC LAYER
SUPPORTING
api.py → mcp_server.py → agent.py
FastAPI backend → MCP health/trend/maintenance/comparison tools → Llama 3.2 tool orchestration and interpretation
__init__.py
Python package initialization and module organization.
Modular design keeps signal processing, diagnostics and agent orchestration independently testable.

## Slide 8
Approach/Algorithms/Tools
Deterministic MCP-Driven AI Agents for Ball Bearing Vibration Diagnostics
ALGORITHMS & APPROACH
SIGNAL → HEALTH → DIAGNOSIS
1 Feature extraction RMS • Kurtosis • Peak-to-Peak • Crest Factor 2 Health assessment Healthy baseline → deviation → robust scaling → rolling median 3 Degradation & trend Degradation index + bounded 0–100 health score + recent slope 4 Prognostic baseline XGBoost RUL regression as an initial baseline
TOOLS & TECHNOLOGIES
IMPLEMENTATION STACK
Python: NumPy, Pandas, SciPy, scikit-learn ML: XGBoost, Joblib Backend: FastAPI, Uvicorn Agentic AI: MCP, Ollama, Llama 3.2 Frontend: HTML, CSS, JavaScript, Chart.js Data: NASA IMS Run-to-Failure Bearing Dataset Development: VS Code, Git/GitHub
Deterministic engineering outputs are exposed through MCP; Llama 3.2 interprets the tool results.

## Slide 9
Findings and Results
Deterministic MCP-Driven AI Agents for Ball Bearing Vibration Diagnostics
Key results
984
NASA IMS observations processed
4
Bearings analyzed
73.28
Highest final degradation — Bearing 1
0.01 / 100
Lowest final health score
WHAT WORKED
MCP diagnostics provide health, trend, maintenance recommendation and bearing comparison. Llama 3.2 converts deterministic results into engineer-facing insights.
WHAT THE BASELINE REVEALED
Initial XGBoost RUL was not sufficiently reliable, indicating the need for trajectory-based prognostics.
Core finding: degradation becomes increasingly visible toward the end of the run.

## Slide 10
Conclusion
Deterministic MCP-Driven AI Agents for Ball Bearing Vibration Diagnostics
From vibration telemetry to maintenance insight
VIBRATION
NASA IMS
FEATURES
Signal indicators
HEALTH
Degradation + score
MCP
Deterministic tools
LLAMA 3.2
Interpretation
END-TO-END
Predictive maintenance prototype from raw bearing vibration to decision support.
EVIDENCE-BASED
High-priority bearings can be identified through health and degradation analysis.
NEXT STEP
Improve prognostics using trajectory-based RUL modeling.

## Slide 11
M.Tech Program
Advanced Industry Integrated Programs
Jointly offered by University and LTIMindTree
Review III
Edge-Optimized RAG and Localized Failure Mitigation for Automated Assembly Lines Using Quantized SLM
Arjun V P
T9987
VIT Chennai
Knowledge partner | Implementation partner

## Slide 12
Introduction
Edge-Optimized RAG and Localized Failure Mitigation
ASSEMBLY-LINE NEED
Fast failure diagnosis is essential to reduce downtime and protect production reliability.
EDGE CONSTRAINT
Cloud AI can introduce latency, connectivity and data-dependency constraints; large models are resource-intensive.
PROPOSED SOLUTION
Edge-optimized RAG + quantized SLM for localized, knowledge-grounded failure mitigation.
LOCAL-FIRST DESIGN
Machine condition → local knowledge retrieval → grounded SLM response → operator-facing mitigation guidance
Goal: practical AI assistance without depending on cloud inference during operation.

## Slide 13
Objective
Edge-Optimized RAG and Localized Failure Mitigation
Project objective
EDGE-OPTIMIZED RAG FOR MACHINE FAILURE DIAGNOSIS
Quantized SLM + local knowledge base + localized mitigation recommendations
FAILURE DIAGNOSIS
Detect machine failure and identify relevant failure modes.
KNOWLEDGE-GROUNDED
Retrieve failure knowledge and maintenance information locally.
EDGE DEPLOYMENT
Reduce latency, compute requirements and cloud dependence.
OPERATOR SUPPORT
Provide real-time mitigation guidance for maintenance decisions.
Design principle: keep inference and supporting knowledge close to the industrial data source.

## Slide 14
Modules to cover
Edge-Optimized RAG and Localized Failure Mitigation
Six-stage EdgeRAG workflow
1. DATA
AI4I → clean
2. CLASSIFY
Healthy / HDF / PWF / OSF / TWF / RNF
3. KNOWLEDGE
Causes + SOPs
4. RETRIEVE
Relevant failure context
5. SLM
Grounded response
6. EDGE
Diagnosis + mitigation
END-TO-END DATA FLOW
Machine Data → Failure Detection → Knowledge Retrieval → Quantized SLM → Diagnosis + Mitigation
The retrieval layer connects model output to evidence before the SLM generates the maintenance response.

## Slide 15
Problem Statement
Edge-Optimized RAG and Localized Failure Mitigation
Why EdgeRAG is needed
PREDICTION ≠ GUIDANCE
ML can predict likely failure but does not automatically provide context-aware maintenance action.
MANUAL KNOWLEDGE SEARCH
Engineers may need to search SOPs, diagnostics and safety instructions manually.
CLOUD DEPENDENCY
Latency, connectivity, privacy and deployment constraints matter in industrial environments.
EDGERAG GAP-FILL
Combine predictive maintenance + local RAG + SLM to transform machine telemetry into an evidence-grounded maintenance report locally.
Result: failure detection is connected directly to relevant maintenance knowledge and recommended action.

## Slide 16
Python Modules
Edge-Optimized RAG and Localized Failure Mitigation
DATA & MODELING
KNOWLEDGE INGESTION
validation.py → train.py → predictor.py → thresholds.py
Quality/label checks → machine-failure & fault-mode training → probabilities → F2-based threshold selection
loader.py → splitter.py → indexer.py → ingest.py
Document loading → recursive chunking → embeddings + Chroma indexing → end-to-end ingestion
RETRIEVAL & PIPELINE
GENERATION & APPLICATION
machine_condition.py → retriever.py
ML output becomes structured machine condition → semantic retrieval + fault-aware reranking + source diversification
generator.py → main.py → config.yaml
Local SLM maintenance report → FastAPI endpoints → configurable models, chunking and retrieval settings
The software structure mirrors the conceptual pipeline: prediction → retrieval → grounded generation.

## Slide 17
Approach/Algorithms/Tools
Edge-Optimized RAG and Localized Failure Mitigation
Architecture and technology stack
AI4I DATA
Validation + preprocessing
RANDOM FOREST
Machine-failure prediction
FAULT MODE
One-vs-Rest + F2 thresholding
CHROMA
Local knowledge retrieval
LOCAL SLM
Evidence-grounded report
RETRIEVAL STACK
LangChain + Ollama + Chroma Recursive chunking • metadata extraction nomic-embed-text embeddings • semantic similarity + fault-aware reranking
APPLICATION STACK
FastAPI + HTML/CSS/JavaScript Local REST API and dashboard connecting machine condition, retrieval and evidence-grounded report generation
Local-first architecture: prediction → retrieval → grounded generation

## Slide 18
Findings and Results
Edge-Optimized RAG and Localized Failure Mitigation
Key results
≈0.97
Test ROC-AUC machine-failure prediction
HDF / PWF / OSF
Major fault modes diagnosed with threshold tuning
TOP RESULTS
Metadata-aware retrieval improved fault relevance
LOCAL
Ollama + Chroma + FastAPI local operation
GENERATION RESULT
The local SLM produces maintenance incident reports grounded in retrieved industrial knowledge, including diagnosis, actions, escalation and restart guidance.
CURRENT LIMITATIONS
TWF prediction and SLM grounding remain limitations and require further model and evaluation refinement.
Core finding: predictive output becomes more useful when tied to fault-aware evidence retrieval.

## Slide 19
Conclusion
Edge-Optimized RAG and Localized Failure Mitigation
EdgeRAG: integrated local decision-support workflow
TELEMETRY
Machine data
ML
Failure + fault mode
RAG
Relevant SOPs
SLM
Evidence-grounded report
ACTION
Mitigation guidance
END-TO-END
Predictive maintenance, RAG and local SLM generation operate in one workflow.
LOCAL-FIRST
Chroma + Ollama provide supporting knowledge and generation without cloud inference.
FUTURE WORK
Improve model efficiency, retrieval evaluation, SLM grounding and edge performance.